## Slide 1: Inductive Sensors
Presented by
Suchithra Ravula
227R1A6249
Cyber Security

## Slide 2: Introduction
Inductive sensors are non-contact devices used to detect metallic objects. They work based on the principle of electromagnetic induction. These sensors are widely used in automation, robotics, and industrial systems.

## Slide 3: Working Principle
• An inductive sensor generates an electromagnetic field using an oscillator.
• When a metallic object enters the field, eddy currents are induced in the object.
• These eddy currents cause energy loss, changing the amplitude of oscillation.
• The sensor’s electronic circuit detects this change and triggers an output signal.

## Slide 4: Main Components
1. Oscillator – Generates an alternating electromagnetic field.
2. Coil – Produces and senses the magnetic field.
3. Detection Circuit – Detects changes in oscillation amplitude.
4. Output Stage – Converts the signal into a usable output.

## Slide 5: Types of Inductive Sensors
1. Unshielded Type – Has a wide sensing range, suitable for non-metallic surroundings.
2. Shielded Type – Electromagnetic field is confined to the front, providing better accuracy.
3. Analog Inductive Sensors – Provide continuous output proportional to distance.
4. Digital Inductive Sensors – Provide discrete ON/OFF output.

## Slide 6: Advantages
• Non-contact operation, minimizing wear and tear.
• High reliability and long service life.
• Resistant to dirt, oil, and water.
• Suitable for harsh industrial environments.

## Slide 7: Limitations
• Can only detect metallic objects.
• Limited sensing distance compared to capacitive sensors.
• Sensitive to temperature variations.
• Costlier than mechanical switches.

## Slide 8: Applications
• Position and speed sensing in automation.
• Metal detection and sorting.
• Industrial machinery control.
• Automotive systems for object detection.

## Slide 9: Summary
Inductive sensors are essential for reliable detection of metallic objects in various industrial applications. Their robustness, accuracy, and maintenance-free operation make them a preferred choice for modern automation systems.

## Slide 10: Thank You